## Slide 1: Correcting sea surface temperature spurious effects in salinity retrieved from spaceborne L-band Radiometer measurements J. Boutin(1), J.L. Vergely(2) , E. Dinnat (3), P. Waldteufel (4), Francesco D’Amico(5), N. Reul(6), A. Supply(1) and Clovis Thouvenin-Masson(1)
(1)
(2)
(6)
(3)
(4)
(5)

## Slide 2: Adjustment of permittivity model
Use SMOS retrieved pseudo-dielectric constant (ACARD) (Waldteufel et al. 2004)
Adjust specific permittivity (α parameter) in Somaraju and Trumpf (ST) model at L-Band:
ACARD SMOS – ACARD KS
using in situ (Argo & ships) SST & SSS, after filtering and correction of conditionnal sampling effect, 5<WS<9m/s,
=>
ST value derived from fits of Ellison, MW’04, Stogryn97 models

## Slide 3: New BV parametrization of dielectric constant
Modelled Tb Adjust specific permittivity (α parameter) in ST model at L-Band:
Boutin et al., 2020
New parametrization => close to KS at moderate SST, variation at low and high T parallel to Zhou at 35 and 33pss (absolute calibration is arbitrary)

## Slide 4: Validation using Aquarius data
MW
MW
KS
BV + SMOS-Liebe93+ SST cond. effect
New BV dielectric constant => |SSSaq-SSSargo| <0.1
(and <0.05 between 5 and 25°C) – similar results when applied in SMOS processing
BV-Liebe 92
BV-SMOS-Liebe 93